## Slide 1: 5G architecture
Icaro Da Silva @ EuCNC 2016, Wednesday, June 29th 14:30 – 16:00

## Slide 2: 1) What are the architecture design principles and building blocks you are working on for 5G era?
Ericsson is leading METIS/METIS-II project, laying the foundation for 5G and establishing the overall 5G RAN. We continue this story as one of the leaders in 5G standardization in 3GPP
New radio (NR) + Evolution of LTE for mMTC, xMBB and URLLC
Next Generation CN being NFV-friendly, even more softwarization, UP/CP separation, full support for e2e network slicing, prepared to serve multiple industries
ICARO : E/// delegate in 3GPP driving 5G architecture topics: tight interworking with LTE, Standalone 5G mobility and initial access (beam-based procedures). Previously leading the Overall control plane design in METIS-II. Active contributor to the 5G PPP architecture WG. Enthusiastic in the area of 5G architecture.

## Slide 3: 2) What are the implementation aspects for the above principles and building blocks?
Anything the connected society needs: standard architecture MUST be flexible
5G mobile Architecture in 3GPP = Next Gen RAN (LTE + NR) and Next Gen CN
Support for uMTC, xMBB, mMTC requirements
Common CN (Next Gen CN)
Common CN/RAN interface (NG2/3 for CP/UP)
Optimized state transitions with no CN signaling
LTE/NR Dual Connectivity
High performing mobility (RAN-based)
Starting point is a simple logical architecture allowing high flexibility with regards to deployment of functions, e.g. distributed / centralized, optimized HW / virtualized
“Please, don’t call me 4G++” 
eLTE eNB
NR gNB
Next Generation CN = 5G CN
NG2/3
NG2/3
Notes: NextGen RAN (NG RAN): radio access network that supports Evolved E-UTRA and/or new radio access technology and interfaces with the next generation core

## Slide 4: 3) What is the standardization roadmap?
Early standard drop in 3GPP with NR connected to LTE via EPC while the Next Generation CN is being designed
Non-Standalone higher layers completion target to be defined in March/2017
Standalone higher layers completion target June/2018
NR gNB Non-Standalone
eLTE eNB
EPC
NR gNB Standalone
eLTE eNB
NG CN
Early drop in 3GPP
Target 5G mobile network architecture
3GPP needs to work on a Migration story to avoid the creation of parallel tracks
NG2/3
S1*
NG2/3

## Slide 5: Overall timeline for NR in TSG-RAN
2. CHECKPOINT: RAN#75: March 2017:
- Completion of SI with corresponding performance evaluation and concepts;
- Approval of WID(s); - Report from RAN1/RAN2/RAN3/RAN4/SA2 on fwd compatibility of NSA and SA NR;
- Reconfirmation of NR timeplan, including completion target for NSA higher layer components (box 4)
4. RAN#78/RAN#79: Stage-3 freeze for Non-Standalone higher layers (including components common with standalone). Completion target TBD.
5. RAN#80, June 2018: Release 15 stage 3 freeze for NR, including Standalone.
1. RAN#73, September 2016:
5G NR Requirements TR completion
2017
2016
3. RAN#78, December 2017:
- Stage 3 freeze of L1/L2 for common aspects of NSA (focused on licensed bands) and SA NR;
- Principles agreed for SA-specific L1/L2 components.
2018
Note: SA: Standalone
NSA: Non-Standalone